## Slide 1
BACHELOR OF ENGINEERING / TECHNOLOGY — ECE CAPSTONE
Edge AI Model Compression Pipeline for Microcontroller Keyword Spotting
Design, INT8 Quantization, and Embedded Deployment Analysis of an Ultra-Compact DS-CNN Targeting the ESP32-S3
Verified Artifacts: 5,248 Parameters | 21.77 KB INT8 FlatBuffer | 54.83% Accuracy | 52.0 KB Working SRAM Host Environment: Windows 11 CPU (Ryzen 3 7320U) | Target: Espressif ESP32-S3 (Virtual Scaffolding)

## Slide 2
FINAL-YEAR ECE PROJECT | EDGE AI
Problem Statement & Edge AI Motivation
1. Cloud Audio Bottlenecks
• High Latency: Round-trip internet transfers introduce 150–1,500 ms delays, preventing real-time control.
• Privacy Hazards: Continuous streaming of private speech over Wi-Fi creates severe eavesdropping risks.
• Bandwidth Overhead: Continuous 16 kHz audio demands ~256 kbps stream per node.
• Network Brittleness: Voice UI fails completely during connection drops or weak signal.
2. MCU Hardware Constraints
• SRAM Scarcity: ESP32-S3 has only 512 KB internal SRAM for runtime heap, stacks, and tensor buffers.
• No Dedicated NPU: Execution relies on Xtensa LX7 dual cores without GPU matrix acceleration.
• Flash Limits: Typical 4 MB SPI Flash must accommodate OTA partitions, Wi-Fi stacks, and code.
• Thermal & Power Budget: Low milliwatt envelope demands minimal clock cycles per inference.
3. The TinyML Solution
• Ultra-Compact Network: DS-CNN with 5,248 parameters (~20.5 KB float weights).
• Full INT8 Quantization: Eliminates software float emulation; uses native SIMD instructions.
• Static Tensor Arena: Predictable 30 KB SRAM buffer with zero dynamic heap allocation.
• Local Autonomy: 100% on-device decision making with zero network dependency.
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 3
FINAL-YEAR ECE PROJECT | EDGE AI
Project Objectives & Execution Scope
Primary Engineering Goals
✔ 12-Class Keyword Spotting: Classify 10 core words ('yes', 'no', 'up', 'down', 'left', 'right', 'on', 'off', 'stop', 'go') + '_silence_' and '_unknown_'.
✔ Deterministic Zero-Leakage Dataset: Curate 4,890 Speech Commands WAVs partitioned strictly by cryptographic speaker hashing.
✔ Full Integer Quantization: Post-training 8-bit integer calibration with full signed int8 input/output tensors.
✔ ESP32-S3 Firmware Scaffold: Generate 8-byte aligned C header (`model_data.h`) and FreeRTOS task with `esp-nn` kernel support.
✔ Comprehensive Memory Budgeting: Model layer-by-layer activation buffers to mathematically size the Tensor Arena.
Scope & Explicit Disclosures
ℹ Host Execution: All model training, evaluation, and dashboard inference were conducted on the host AMD Ryzen 3 7320U CPU.
ℹ Microcontroller Estimates: ESP32-S3 latency (~6–10 ms) is an analytical projection from literature, not on-silicon measurement.
ℹ Firmware Compilation Status: ESP-IDF source files and CMake configs are syntactically validated, but the compiler (`idf.py`) is not installed on this host (Template Only / Not Built).
ℹ Physical Hardware: Flashing to physical silicon, battery current draw, and hardware audio capture were NOT performed.
ℹ Reproducibility: 100% of reported numbers originate from verified disk artifacts and a 61-test automated suite.
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 4
FINAL-YEAR ECE PROJECT | EDGE AI
End-to-End System Pipeline & Data Flow
Step 1: Audio Preprocessor
16 kHz Mono WAV (1.0s)
16,000 samples
Pre-emphasis (α=0.97)
Hann windowing (25ms)
Stride (20ms) -> 47 frames
40 Mel-filterbank DCT
Step 2: DS-CNN Baseline
Feature map: [1, 40, 47]
5,248 parameters
Standard Conv (28 filters)
2× Depthwise-Pointwise blocks
Global Pooling + Linear
PyTorch FP32 State Dict
Step 3: INT8 Quantization
Post-Training Quantization
100-sample calibration set
Full int8 input & output
S_in = 0.4796, Z_in = 54
S_out = 0.1009, Z_out = 82
TFLite FlatBuffer (21.77 KB)
Step 4: ESP32-S3 Scaffold
Aligned C Header (alignas 8)
SHA-256 Verified
30 KB Tensor Arena
FreeRTOS Task Architecture
ESP-NN Vector Kernels
52.0 KB Working SRAM
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 5
FINAL-YEAR ECE PROJECT | EDGE AI
Dataset Integrity & MFCC Feature Extraction
Deterministic Speaker-Isolated Dataset
Dataset Source: Google Speech Commands v2 (4,890 verified WAV files, 149.44 MB).
12 Target Classes: 10 commands ('yes', 'no', 'up', 'down', 'left', 'right', 'on', 'off', 'stop', 'go') + '_silence_' (ambient noise) + '_unknown_' (19 other words).
Speaker Isolation Mechanism: SHA-1 hash of speaker ID guarantees 0.0% speaker overlap between splits:
• Training: 3,936 clips (829 unique speakers)
• Validation: 436 clips (98 unique speakers)
• Held-out Test: 518 clips (102 unique speakers)
Zero-Leakage Guarantee: Prevents neural memorization of individual vocal timbres.
MFCC Signal Processing Chain
Sampling Rate: 16,000 Hz, 16-bit PCM, single-channel mono.
Framing: 25 ms window (400 samples) with 20 ms stride (320 samples) -> 47 time frames.
Windowing: Periodic Hann window to suppress spectral leakage.
Spectral Analysis: 512-point FFT -> 40 triangular Mel-scale filterbanks (20 Hz to 4,000 Hz).
Log Energy & DCT: Type-II Discrete Cosine Transform extracts 40 orthogonal cepstral coefficients.
Output Feature Tensor: Shape [1, 40, 47] (1,880 total elements per 1.0 second audio clip).
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 6
FINAL-YEAR ECE PROJECT | EDGE AI
DS-CNN Architecture & Baseline FP32 Model
Layer Type | Kernel / Stride | Params | Output Shape
Input Feature | — | 0 | [1, 40, 47, 1]
Conv2D + BN + ReLU | 3×3, Stride 2 | 336 | [1, 20, 24, 28]
Depthwise Conv 1 | 3×3, Stride 1 | 336 | [1, 20, 24, 28]
Pointwise Conv 1 | 1×1, Stride 1 | 868 | [1, 20, 24, 28]
Depthwise Conv 2 | 3×3, Stride 1 | 336 | [1, 20, 24, 28]
Pointwise Conv 2 | 1×1, Stride 1 | 868 | [1, 20, 24, 28]
AdaptiveAvgPool + Linear | Pool + FC | 348 | [1, 12]
Training Configuration
Parameter Budget: Exactly 5,248 trainable weights.
Separable Advantage: ~8.7× computational saving over traditional 2D convolutions.
Optimizer: Adam (lr = 0.001) with CrossEntropyLoss.
Batch Size: 64 samples over 8 completed epochs.
Augmentation: Time-shift jitter (±100 ms) and background ambient noise mixing.
Checkpoint: Saved at models/checkpoints/baseline_dscnn.pt (102.93 KB state_dict).
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 7
FINAL-YEAR ECE PROJECT | EDGE AI
Full INT8 Integer Quantization Workflow
Quantization Formulation
Uniform Affine Mapping: Continuous FP32 values x are mapped to signed 8-bit integers q in [-128, 127]: q = clamp(round(x / S) + Z, -128, 127)
Scale (S) & Zero-Point (Z): S = (x_max - x_min) / 255 Z = round(-128 - x_min / S)
Full Integer Constraint: Both model input and output tensors are constrained strictly to int8, eliminating float conversion wrappers.
Input Quantization Params: S = 0.479577, Z = 54
Output Quantization Params: S = 0.100918, Z = 82
TFLM & ESP-NN Compatibility
Representative Calibration: Calibrated using 100 genuine training audio clips to record dynamic activation ranges.
Zero-Copy Kernels: All 5 model operator types are verified compatible with TFLM and Espressif esp-nn assembly:
• CONV_2D (Xtensa PIE vector accelerated)
• DEPTHWISE_CONV_2D (Xtensa PIE vector accelerated)
• FULLY_CONNECTED (Xtensa PIE vector accelerated)
• AVERAGE_POOL_2D (Integer pooled)
• RESHAPE (Metadata pointer adjustment)
Zero Unsupported Fallbacks: 100% of network executes in hardware-friendly integer arithmetic.
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 8
FINAL-YEAR ECE PROJECT | EDGE AI
Verified Benchmark Results: FP32 vs Full INT8
MODEL FILE SIZE
21.77 KB
-78.85%
From 102.93 KB (.pt) to 21.77 KB (.tflite)
TEST ACCURACY
54.83%
-0.58 pp
55.41% (FP32) vs 54.83% (INT8) on 518 samples
MACRO-F1 SCORE
0.5179
+0.0069
FP32: 0.5110 -> INT8: 0.5179 (+0.69 pp)
LAPTOP CPU LATENCY
0.30 ms
7.59× Speed
2.29 ms (FP32) -> 0.30 ms (INT8) (XNNPACK)
Metric | Baseline PyTorch FP32 | Quantized TFLite INT8 | Difference / Compression | Verification Status
Model Disk Size | 105,396 B (102.93 KB) | 22,296 B (21.77 KB) | -78.85% (4.73× compression) | Exact file bytes
Raw Weight Payload | 20,992 B (20.50 KB) | 5,248 B (5.125 KB) | -75.00% (4.00× compression) | 5,248 parameters
Test Accuracy (518 clips) | 55.41% (287 / 518) | 54.83% (284 / 518) | -0.58 percentage points | Identical test set
Host CPU Latency | 2.29 ms ± 0.96 ms | 0.30 ms ± 0.08 ms | 7.59× speedup / 3,312 inf/sec | Ryzen 3 7320U (100 runs)
Latency measured on host AMD Ryzen 3 7320U CPU. Identical 518 test clips evaluated.

## Slide 9
FINAL-YEAR ECE PROJECT | EDGE AI
Interactive Reviewer Dashboard (Local Web App)
Architecture & Implementation
Framework: Local Streamlit web application running at http://localhost:8501.
Crash-Resistant PyArrow-Free Tables: Direct HTML table serialization prevents numpy version collisions.
Sandbox File Security: Strict path traversal prevention restricts report downloads to results/reports/.
Graceful Fallback: Corrupted or missing artifacts display informative warning badges without crashing.
Automated Verification: Browser automation subagent verified all 5 pages and rendered tables.
Key Reviewer Capabilities
1. Audio Inference Lab: Select real WAV samples across all 12 classes; view waveform and MFCC feature spectrograms.
2. Live Dual Model Prediction: Concurrently runs PyTorch FP32 and TFLite INT8 on user-selected audio.
3. Side-by-Side Model Comparison: Live tables displaying accuracy, F1, size, parameter counts, and latency deltas.
4. Visualizations: Interactive confusion matrices (100% precision on '_silence_'), training loss curves, and latency charts.
5. Virtual ESP32 Analysis: Layer-by-layer activation dimensions and SRAM budget calculators.
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 10
FINAL-YEAR ECE PROJECT | EDGE AI
Virtual ESP32-S3 Deployment & Resource Budget
Subsystem Component | Memory Type | Size | % of Resource
Model FlatBuffer Payload | Flash (.rodata) | 21.77 KB | 0.54% of 4 MB Flash
Tensor Arena (Activations) | Internal SRAM | 30.00 KB | 5.86% of 512 KB SRAM
KWS Task Stack (FreeRTOS) | Internal SRAM | 16.00 KB | 3.13% of 512 KB SRAM
I2S DMA Audio Buffers | Internal SRAM | 2.00 KB | 0.39% of 512 KB SRAM
MFCC Scratchpad Buffer | Internal SRAM | 4.00 KB | 0.78% of 512 KB SRAM
Total Working SRAM | Internal SRAM | 52.00 KB | 10.16% (89.8% Headroom)
Activation Double-Buffering
Memory Planner: TFLM dynamically reuses buffers between non-overlapping operations.
Peak Adjacent Buffers: Conv2D (13,440 B) + Depthwise Conv (13,440 B) = 26,880 bytes (26.25 KB).
TFLM Metadata & Padding: 2,048 bytes (2.00 KB).
Minimum Theoretical Arena: 28,928 bytes (28.25 KB).
Configured Tensor Arena: 30,720 bytes (30.00 KB) provides +10.7% safety margin.
Projected ESP32-S3 Latency: ~6–10 ms @ 240 MHz utilizing esp-nn vector extensions.
Analytical estimates. Flash/SRAM computed mathematically. Physical ESP32 flashing not performed.

## Slide 11
FINAL-YEAR ECE PROJECT | EDGE AI
Technical Limitations & Future Work
Current Engineering Disclosures
• Laptop Latency Baseline: 0.30 ms latency was measured on an x86 laptop CPU; embedded on-silicon latency will be higher (~6–10 ms).
• Firmware Build Status: The ESP-IDF toolchain ('idf.py') is not installed on this host. CMake files and C++ firmware are syntactically validated but uncompiled.
• Zero Physical Hardware: Power dissipation (mA), acoustic microphone background noise, and physical GPIO actions were not tested on hardware.
• Uncalibrated Pruning: Structured channel pruning and knowledge distillation were designed conceptually but excluded from this baseline.
Roadmap for Physical Validation
• 1. Toolchain Installation: Set up ESP-IDF v5.1+ and Xtensa GCC toolchain to build flashable .bin binaries.
• 2. Development Board Flashing: Flash compiled binary to ESP32-S3-DevKitC-1 via USB-JTAG.
• 3. I2S MEMS Microphone: Interface INMP441 digital microphone for live continuous listening.
• 4. Power & Current Profiling: Measure dynamic milliwatt power draw using shunt resistor and oscilloscope.
• 5. Advanced Compression: Integrate L1 structured filter pruning and Knowledge Distillation from a larger ResNet-18 teacher.
Host: AMD Ryzen 3 7320U CPU | Target: ESP32-S3 (Virtual) | 61/61 Automated Tests Passing

## Slide 12
FINAL-YEAR ECE PROJECT SUMMARY
Key Takeaways & Conclusion
1. Extreme Compression with Parity: 78.85% model size reduction (102.9 KB -> 21.77 KB) with only 0.58 pp accuracy loss (54.83%). 2. Microcontroller Feasibility: Occupies 0.54% of 4 MB Flash and 52.0 KB working SRAM (89.84% free headroom on ESP32-S3). 3. Cryptographic C-Export: Generated model_data.h verified with 100% byte-for-byte SHA-256 integrity. 4. Full Transparency: Complete separation between measured PC benchmarks and analytical embedded estimates. 5. Rigorous Quality: 61 automated unit/integration tests passing with 0 failures. Thank You. Questions & Discussion Welcome.